## Slide 1
Spacecraft Communications
ENAE 694
Noise and the Complete Link Budget
Dave Israel (disrael@umd.edu)
October 5, 2026

## Slide 2
Received Power Is Only Half the Story
ENAE 694 • Noise and the Link Budget
3
Desired signal
Received power S
Noise density
N0 in W/Hz
Receiver
Both arrive
together
Compare
S/N0
S/N0 compares received signal power with noise per hertz.

## Slide 3
Room-Temperature Noise
Question: Will the Receiver Read Zero?
ENAE 694 • Noise and the Link Budget
4
Room-temperature
noise source
290 K*
No transmitted
signal
Receiver
Noise bandwidth B
Power measurement
Thermal motion creates random electrical fluctuations.
What power reaches the receiver?
* Matched connection: the receiver accepts the source’s available noise power.

## Slide 4
Room-Temperature Noise
Random Fluctuations Carry Real Power
ENAE 694 • Noise and the Link Budget
5
Noise voltage versus time
Noise density versus frequency
No repeating cycle.
Mean voltage is approximately zero.
Collected area
N = kTB
Height: N0 = kT
Width: B hertz
The squared fluctuations have a positive average: the noise power is real.

## Slide 5
Thermal Noise Density: N0 = kT
Thermal noise has density N0 = kT, in W/Hz.
[N0] = −228.6 + 10 log10(T/K), in dBW/Hz.
At 290 K: [N0] = −204.0 dBW/Hz = −174.0 dBm/Hz.
Doubling T raises the noise density by 3.0 dB.
Total noise across bandwidth B is N = N0B = kTB.
ENAE 694 • Noise and the Link Budget
6

## Slide 6
Noise Figure: The Component Specification
A component adds noise and degrades the input SNR.
Noise factor measures that degradation: F = SNRin/SNRout.*
Noise figure expresses it in dB: NF = 10 log10F.
Lower NF means less added noise under the same conditions.
Component noise figure and gain describe each receiver stage.
ENAE 694 • Noise and the Link Budget
7
* NF uses a source at T₀ = 290 K and the same noise bandwidth at input and output.

## Slide 7
Three Different Meanings of Temperature
ENAE 694 • Noise and the Link Budget
8
Physical temperature
Tphysical
Actual hardware temperature.
A thermometer could measure it.
Example: 290 K
Equivalent noise temperature
Te
Receiver-added noise expressed
as an equivalent input temperature.
Example: 50 K
Reference temperature
T0
The fixed convention for defining
noise factor and noise figure.
Always 290 K
One receiver can have 290 K hardware, 50 K equivalent noise, and a 290 K reference.

## Slide 8
Equivalent Noise Temperature
A Useful Way to Describe Added Noise
ENAE 694 • Noise and the Link Budget
9
1. Noise arrives
The receiver amplifies the incoming noise.
2. The receiver adds noise
The output contains both contributions.
3. Express that addition at the input
Te tells us the strength of an equivalent thermal source.
NF = 0.69 dB gives Te = 290(10NF/10 − 1) ≈ 50 K.

## Slide 9
Equivalent Noise Temperature
Two Models, Exactly the Same Output
ENAE 694 • Noise and the Link Budget
10
ACTUAL RECEIVER
Input signal
+ source noise
Physical receiver
Gain G; adds noise
Output signal
+ total noise
EQUIVALENT CALCULATION MODEL
Same input
+ equivalent added density
kTe
Noiseless amplifier
Same gain G
Same output
signal and noise
We relocate added noise in the model. The hardware and its output are unchanged.

## Slide 10
Equivalent Noise Temperature
Which Noise Contribution Matters Most?
ENAE 694 • Noise and the Link Budget
11
Same receiver: NF = 0.69 dB.
Convert once: Te ≈ 50 K for the system-noise sum.*
Cold-sky source: 30 K
Tsys = 80 K (19.0 dB-K)
Receiver noise is the larger part.
Room-temperature source: 290 K
Tsys = 340 K (25.3 dB-K)
Source noise is the larger part.
Lowering receiver noise helps most when receiver noise dominates.
* Equivalent-input model: JPL DESCANSO, Vol. 10, Ch. 2. The added source is a calculation model.

## Slide 11
Antenna Noise Need Not Be 290 K
ENAE 694 • Noise and the Link Budget
Same receiver: NF = 0.69 dB
290 K source
340 K (25.3 dB-K)
30 K source
80 K (19.0 dB-K)
Source
Receiver-added
Lower antenna noise gives lower total noise with the same receiver NF.
12

## Slide 12
Antenna Noise: The Practical Picture
ENAE 694 • Noise and the Link Budget
13
The antenna collects noise as well as the wanted signal.
Sky, atmosphere, ground, and the Moon can change TA.
The antenna pattern and pointing determine how much enters.
Use a specified antenna temperature for the link calculation.
Keep external antenna noise separate from receiver noise figure.

## Slide 13
Reference Planes in the Receiving System
ENAE 694 • Noise and the Link Budget
14
Antenna
collects signal
and scene noise
Receive feed
1 dB loss
290 K physical
Receiver / LNA
NF = 0.69 dB
(Te ≈ 50 K)
Plane A
Plane B
Antenna terminal
[SA], Tsys,A
Receiver input
[SB], Tsys,B
Use signal and total equivalent noise at the same plane.

## Slide 14
Antenna Temperature
The Pattern Weights the Whole Scene
ENAE 694 • Noise and the Link Budget
15
Sky brightness
Tsky
Ground brightness
Tground
Antenna pattern
weights each direction
then sums the noise*
Antenna port
N0 = kTA
Sky temperature describes radiation from a direction.
Antenna temperature describes the noise delivered at the port.
* Lossless-antenna model. Source: Condon & Ransom, Essential Radio Astronomy, Ch. 3.

## Slide 15
Antenna Temperature
Question: How Much Does Ground Matter?
ENAE 694 • Noise and the Link Budget
16
Sky: 10 K
95% pattern weight
Ground: 290 K
5% pattern weight
Weighted sum
Σ*
Antenna port
TA = ?
* Lossless antenna. Weights represent integrated antenna response in each region.

## Slide 16
Antenna Temperature
Worked Answer: The Weighted Noise
ENAE 694 • Noise and the Link Budget
TA = Σ wiTi (lossless antenna)
Sky: 0.95 × 10
9.5 K
Ground: 0.05 × 290
14.5 K
TA = 0.95(10) + 0.05(290) = 24.0 K
The 5% ground pickup contributes more noise than the 95% sky pickup.
17

## Slide 17
The Moon and Antenna Beam Coupling
ENAE 694 • Noise and the Link Budget
18
OFF the Lunar Disk
ON the Lunar Disk
Assume TA = 30 K*
Assume TA = 230 K
* Assumed scene temperatures. Beam outlines are schematic. Moon image: NASA SVS / LRO.

## Slide 18
Atmosphere at 270 K
Question: What Reaches the Antenna?
ENAE 694 • Noise and the Link Budget
19
Incoming signal
+ background noise
Tbackground = 3 K
Absorbing layer
0.1 dB loss
270 K physical
Thermal emission*
Signal: lower
Noise: ?
Antenna input
The layer attenuates incoming radiation and generates its own thermal noise.
* Isothermal layer model. Sources: NRAO Essential Radio Astronomy, Ch. 1; DSN 810-005.

## Slide 19
Atmosphere at 270 K
Worked Answer: Loss and Emission
ENAE 694 • Noise and the Link Budget
20
Transmitted background
Tbg × 10−A/10
3 × 10−0.1/10 ≈ 2.93 K
Layer emission
Tphys(1 − 10−A/10)
270(1 − 10−0.1/10) ≈ 6.15 K
Total
9.1 K
Noise seen
by antenna
Signal ledger: [Sout] = [Sin] − 0.1 dB
Tseen = Tbg10−A/10 + Tphys(1 − 10−A/10) ≈ 9.1 K.

## Slide 20
Weather and Frequency
Atmospheric Absorption
ENAE 694 • Noise and the Link Budget
21
Water vapor has a feature
near 22 GHz.
Oxygen absorbs strongly
around 60 GHz.
Cloud liquid water adds loss.
Dry, high sites reduce water
along the atmospheric path.
This curve is gas/cloud opacity,
not rain attenuation.*
* Green Bank summer example. Attenuation in dB = 4.3 × opacity τ. Source: Condon & Ransom, Fig. 1.2.

## Slide 21
Weather and Frequency
Rain Attenuation
ENAE 694 • Noise and the Link Budget
22
0
2
4
6
8
0.4
12
1.1
20
2.8
30
5.1
Specific attenuation (dB/km)
Frequency (GHz)
Same rain rate: 25 mm/h.*
For these microwave bands,
higher frequency gives much
more rain attenuation.
Total fade also depends on
rain-path length and elevation.
Ka-band generally needs more
rain margin than X-band.
* ITU-R P.838-3, Table 5; horizontal polarization. Connected model samples, not station fade predictions.

## Slide 22
Weather and Ground Stations
Rain Margin and Site Selection
ENAE 694 • Noise and the Link Budget
23
Rain margin is extra allowance for weather fades at a chosen availability.
Choose it using frequency, local rain statistics, elevation, and path geometry.
Dry climates and high sites often reduce atmospheric attenuation and noise.
Higher elevation shortens the path through the lower atmosphere.
Site diversity can keep service available when rain affects one station.*
Weather reduces S and can raise antenna noise, lowering G/T.
* ITU-R P.618-14. Required S/N₀ and adequacy come later; no universal rain margin is assigned here.

## Slide 23
What Attenuates Signal? What Adds Noise?
ENAE 694 • Noise and the Link Budget
24
Mechanism
Signal
Noise
Free space, pointing,
polarization mismatch
Less received power
No thermal emission
implied by this loss
Room-temperature feed /
absorbing atmosphere
Attenuated
Incoming noise attenuated;
thermal emission added
Receiver amplifier
Amplified
Incoming noise amplified;
receiver noise added

## Slide 24
Break
ENAE 694 • Noise and the Link Budget
25

## Slide 25
Lunar Link
Feed Loss and Noise at Two Planes
ENAE 694 • Noise and the Link Budget
26
Room-temperature feed
1.0 dB loss
290 K physical
A: feed input
B: feed output
Antenna noise: 30 K
Signal: [SA]
Signal: [SA] − 1 dB
Antenna noise: 23.8 K
Feed noise referred to input A:
(Lf − 1)Tphysical = 75.1 K
Feed noise delivered at output B:
(1 − 1/Lf)Tphysical = 59.6 K
Lf = 10[L_f]/10. Both terms represent the same feed noise at different planes.

## Slide 26
Lunar Link
One System, Two Noise Ledgers
ENAE 694 • Noise and the Link Budget
27
Contribution
At A: before feed
At B: after feed
Antenna
30.0 K
23.8 K
Feed emission
75.1 K
59.6 K
Receiver
63.0 K
50.0 K
Tsys
[Tsys]
168.0 K
22.3 dB-K
133.5 K
21.3 dB-K
A to B: [S] and [Tsys] both fall 1.0 dB. [S/N0] stays unchanged.
Tsys,A = TA + (Lf − 1)Tphys + LfTe,rx; Tsys,B = Tsys,A/Lf

## Slide 27
Receiver Cascade
Where Each Stage Adds Noise
ENAE 694 • Noise and the Link Budget
28
Source
Signal + kTA per Hz
LNA
Gain [G1], NF1
Later receiver
Gain [G2], NF2
Source noise passes through both stages.
Each stage also adds its own noise.
The LNA boosts the signal before later stages add their noise.
That makes later-stage noise less important relative to the signal.
Input referral expresses all added noise at one common reference plane.

## Slide 28
Receiver Cascade
The Model: Friis Noise Equations
1. Convert catalog values: F = 10NF/10, G = 10[G]/10.
2. Combine the stages using their linear factors:
Ftotal = F1 + (F2 − 1)/G1 + (F3 − 1)/(G1G2) + …
3. Return to dB: NFtotal = 10 log10Ftotal.
The first stage enters directly. Early gain reduces later terms.
ENAE 694 • Noise and the Link Budget
29

## Slide 29
Receiver Cascade
Question: How Much Early Gain Helps?
LNA NF = 0.68 dB. Following receiver NF = 6.48 dB.
Keep both noise figures fixed as LNA gain changes.
Calculate combined NF for LNA gains of 10, 20, and 30 dB.
How much improvement does each extra 10 dB provide?
What sets the limit as LNA gain becomes very large?
ENAE 694 • Noise and the Link Budget
30

## Slide 30
Receiver Cascade
Worked Answer: 10, 20, and 30 dB Gain
Fi = 10NF_i/10; G1 = 10[G_1]/10; NFtotal = 10 log10Ftotal.
Ftotal = F1 + (F2 − 1)/G1 ≈ 1.17 + 3.45/G1.
10 dB: G1 = 10; NFtotal ≈ 1.8 dB.
20 dB: G1 = 100; NFtotal ≈ 0.80 dB.
30 dB: G1 = 1000; NFtotal ≈ 0.69 dB.
The limit is the first LNA’s NF ≈ 0.68 dB.
ENAE 694 • Noise and the Link Budget
31

## Slide 31
Receiver Cascade
From Component noise figure to the Link Budget
ENAE 694 • Noise and the Link Budget
32
LNA
Gain: 30 dB
NF: 0.68 dB
Following receiver
NF: 6.48 dB
Cascade NF ≈ 0.69 dB.
Convert once for G/T: Te,rx = 290(Ftotal − 1) ≈ 50 K.
NF is the component figure of merit; kelvins combine receiver and antenna noise.

## Slide 32
Receiver Components
Reading an LNA Datasheet
ENAE 694 • Noise and the Link Budget
33
The catalog gives NF and gain
at specified frequencies and bias.
This PGA-103+ example lists:
NF: 0.6 dB at 1 GHz
NF: 0.9 dB at 2 GHz
Gain: 11 dB at 2 GHz
Also check power, matching,
linearity, and operating band.*
* Catalog-reading example, not the 8.4 GHz link LNA. Mini-Circuits PGA-103+ datasheet; image hosted by LCSC.

## Slide 33
LNA Placement
Question: Where Should the LNA Go?
ENAE 694 • Noise and the Link Budget
34
Source: 30 K. Cable: 290 K physical. LNA NF: 0.69 dB.
A
Cable: 3.0 dB loss*
LNA: 20 dB gain
B
LNA: 20 dB gain
Cable: 3.0 dB loss
Both give 20 − 3.0 = 17.0 dB signal gain.
Will they give the same output noise?
* Cable loss is exactly half power (3.0 dB). A/B identify arrangements on this slide.

## Slide 34
LNA Placement
Worked Answer: Both Component Orders
ENAE 694 • Noise and the Link Budget
35
Friis: Ftotal = F1 + (F2 − 1)/G1; NFtotal = 10 log10Ftotal.
A
Cable: 3.0 dB loss
LNA: 20 dB gain
B
LNA: 20 dB gain
Cable: 3.0 dB loss
Cable first: Ftotal = 2 + (FLNA − 1)/0.5; NFtotal ≈ 3.7 dB.
LNA first: Ftotal = FLNA + (2 − 1)/100; NFtotal ≈ 0.73 dB.
Combined receiver NF: 3.7 dB with cable first; 0.73 dB with LNA first.
NF improvement ≈ 3.0 dB, using the 290 K reference source.*
* Matched 290 K cable: F = 2, G = 0.5. LNA: F ≈ 1.17, G = 100.

## Slide 35
LNA Placement
Why Our Link Improves by 7.0 dB
ENAE 694 • Noise and the Link Budget
36
Te,total = 290(Ftotal − 1); Tsys = Tsource + Te,total.
Cable first adds 390 K. LNA first adds 52.9 K.
NF compares both arrangements with a 290 K reference source:
10 log10[(290 + 390)/(290 + 52.9)] ≈ 3.0 dB.
Our antenna has only 30 K, so the actual [S/N0] improves by:
10 log10[(30 + 390)/(30 + 52.9)] ≈ 7.0 dB.
* Same signal gain in both arrangements. A quieter antenna makes receiver-added noise more important.

## Slide 36
LNA Placement
What It Means for Receiver Layout
ENAE 694 • Noise and the Link Budget
37
Antenna
feed
Low-noise
amplifier
Long cable
and later receiver
Shortest practical
low-loss connection
Low LNA noise figure sets a low receiver-noise floor.
Enough early gain reduces later input-referred noise.
Check overload, stability, bandwidth, and input filtering.*
* Design guidance: JPL DESCANSO, Vol. 10, Ch. 2; Analog Devices AN-2622.

## Slide 37
Why DSN Uses Cryogenic LNAs
ENAE 694 • Noise and the Link Budget
38
Low-Noise Amplifier (LNA)
A refrigerator cools the LNA.
Physical cooling can lower its NF
and receiver-added noise.*
Physical Cooling, Lower Noise
A lower LNA NF reduces the receiver contribution.
The remaining antenna and feed noise limit
the improvement in total system sensitivity.
* Cryogenic LNA sources: JPL DESCANSO Ch. 5; S10. DSN photo: NASA/JPL-Caltech, PIA17791.

## Slide 38
Receiving Sensitivity: G/T
G/T is the receiving system’s figure of merit.
Combine receive antenna gain with total system noise.
[Tsys] = 10 log10(Tsys/K), in dB-K.
[G/T] = [Gr] − [Tsys], in dB/K.*
A 1.0 dB gain in [G/T] adds 1.0 dB to [S/N0].
ENAE 694 • Noise and the Link Budget
39
* Use antenna-system gain and total noise at the same plane. Hold other link terms fixed.

## Slide 39
Lunar Link
Worked Example: Cryogenic Cooling
ENAE 694 • Noise and the Link Budget
Receiver NF: 0.69 to 0.15 dB.* Te = 290(10NF/10 − 1).
Te,rx: about 50 K to 10 K.
Tsys,A = TA + (Lf − 1)Tphys + LfTe,rx.
168.0 K (22.3 dB-K) becomes 117.7 K (20.7 dB-K).
Δ[G/T] = Δ[S/N0] = 10 log10(168.0/117.7) ≈ 1.5 dB.
40
* Illustrative receiver specifications. Equivalent noise temperature differs from hardware temperature.

## Slide 40
Improving Sensitivity
Question: Which Change Helps?
A. Increase receive antenna gain by 3 dB; hold Tsys fixed.
B. Halve total system noise temperature; hold gain fixed.
C. Add 20 dB of ideal gain after the receiver.
Which changes G/T and S/N0? Which changes only output levels?
ENAE 694 • Noise and the Link Budget
41

## Slide 41
Improving Sensitivity
Worked Answer: Gain versus Noise
A. Adding 3 dB of antenna gain raises [G/T] and [S/N0] by 3 dB.
B. Halving Tsys raises [G/T] and [S/N0] by 3.0 dB.
C. Ideal final gain raises signal and noise equally. The ratio is unchanged.
Sensitivity improves when more signal is collected or less noise is added.
ENAE 694 • Noise and the Link Budget
42

## Slide 42
Lunar Link
Example Inputs and Assumptions
ENAE 694 • Noise and the Link Budget
43
384,400 km
Spacecraft → Earth
8.4 GHz return link
1 W transmitter
0.3 m TX dish
34 m receive dish
Aperture efficiency 0.55
* Illustrative link assumptions. Images: NASA SVS / LRO; NASA/JPL-Caltech, PIA17791.
TX line: 0.60 dB. TA = 30 K. Feed: 1 dB at 290 K.
Receiver NF = 0.69 dB (Te,rx ≈ 50 K). Off the lunar disk.*

## Slide 43
Lunar Link
The Tools: Antenna Gain and Path Loss
G = η(πDf/c)2
For η = 0.55:
[G] = 17.8 + 20 log10(D/m) + 20 log10(f/GHz)
[Lp] = 92.4 + 20 log10(R/km) + 20 log10(f/GHz)
Use diameter in meters and range in kilometers.
ENAE 694 • Noise and the Link Budget
44

## Slide 44
Lunar Link
Question: Build the Signal Budget
Let’s calculate [Gtx], [Gr], and [Lp].
Other losses: 0.1 dB atmosphere + 0.8 dB pointing
+ 0.5 dB polarization = 1.4 dB.
Where do the 0.6 dB TX loss and 1 dB receive-feed loss go?
At terminal A, has the signal passed through the receive feed?
ENAE 694 • Noise and the Link Budget
45

## Slide 45
Lunar Link
Worked Answer: Signal Power at A
Transmitter power
+0.0 dBW
Transmitter line loss
−0.6 dB
Transmit antenna gain
+25.8 dBi
Free-space loss
−222.6 dB
Atmosphere + pointing + polarization
−1.4 dB
Receive antenna gain
+66.9 dBi
Received SA*
−131.9 dBW
ENAE 694 • Noise and the Link Budget
46
* Plane A precedes the receive feed. At B, the signal is 1 dB lower.
[SA] = [Ptx] − [Ltx] + [Gtx] − [Lp] − [Lother] + [Gr]

## Slide 46
Lunar Link
Worked Answer: System Noise at A
ENAE 694 • Noise and the Link Budget
All noise referred to antenna terminal A
30.0
75.1
62.9
Antenna
Feed emission
Receiver via feed
[Tsys,A] = 10 log10(168.0) = 22.3 dB-K.
[G/T]A = [Gr] − [Tsys,A] ≈ 44.7 dB/K.
47
Lf = 101.0/10; Tsys,A = TA + (Lf − 1)Tphys + LfTe,rx.
Feed: (Lf − 1)290 ≈ 75.1 K; receiver via feed: Lf(50) ≈ 62.9 K.

## Slide 47
Lunar Link
Worked Answer: Signal-to-Noise Density
N0,A = kTsys,A; [N0,A] = [k] + [Tsys,A].
With [k] = −228.6: [N0,A] ≈ −206.35 dBW/Hz.
[S/N0] = [SA] − [N0,A].
= −131.87 − (−206.35) = 74.48 ≈ 74.5 dB-Hz.
ENAE 694 • Noise and the Link Budget
48

## Slide 48
When Bandwidth Is Needed
N0 tells us the noise power per hertz.
Bandwidth B tells us how much noise a receiver or instrument admits.
We need total noise N = N0B to compare measured powers as S/N.
[S/N] = [S/N0] − 10 log10(B/Hz).
At 1 MHz: [S/N] = 74.5 − 60.0 = 14.5 dB.*
ENAE 694 • Noise and the Link Budget
49
* Narrowing B helps only while passing the needed signal. Use equivalent noise bandwidth.

## Slide 49
Lunar Link
The Complete Budget in One View
ENAE 694 • Noise and the Link Budget
50
TRANSMIT
[EIRP] = 25.2 dBW
PROPAGATE
Free space: −222.6 dB
Other losses*: −1.4 dB
COLLECT
+66.9 dBi
[SA] = −131.9 dBW
NOISE AT A
Tsys = 168.0 K
[Tsys] = 22.3 dB-K
[N0] = −206.3 dBW/Hz
COMPARE
[S/N0] = 74.5 dB-Hz
DESIGN TRADES
More EIRP or G/T helps
More propagation loss hurts
This is the calculated S/N0. Modulation will determine what value is sufficient.
* Other losses: atmosphere 0.1 dB + pointing 0.8 dB + polarization 0.5 dB.

## Slide 50
Lunar Link
What Changes When We Point at the Moon?
ENAE 694 • Noise and the Link Budget
51
Same Signal Power
TA: 30 K to 230 K
Tsys,A: 168.0 K to 368.0 K
[Tsys,A]: 22.3 to 25.7 dB-K*
Tsys,new = Tsys,old + (230 − 30) = 368.0 K.
Δ[S/N0] = −10 log10(368.0/168.0) = −3.4 dB.
[S/N0]new = 74.5 − 3.4 = 71.1 dB-Hz.
* Assumed antenna temperatures at fixed signal power. Visible-light Moon image: NASA SVS / LRO.

## Slide 51
Lunar Link
Questions: What Changes in the Budget?
1. Double received signal power; hold noise density fixed.
2. Double range; hold antenna gains and temperatures fixed.
3. Double Tsys; hold the signal budget fixed.
4. Add 0.5 dB atmospheric loss. Does N0 also change?
ENAE 694 • Noise and the Link Budget
52

## Slide 52
Lunar Link
Worked Answers: Changes in S/N0
Double S: Δ[S/N0] = 10 log10(2) = +3.0 dB.
Double range: Δ[Lp] = 20 log10(2) = +6.0 dB.
Double Tsys: Δ[G/T] = −10 log10(2) = −3.0 dB.
Weather: Δ[S/N0] = −Δ[Latm] + Δ[G/T].*
Update both atmospheric signal loss and antenna noise.
ENAE 694 • Noise and the Link Budget
53
* Other link terms held fixed. Atmospheric emission can change G/T.

## Slide 53
Questions for a Ground-Network Provider
What is G/T at our frequency, elevation, and weather condition?
Which losses and reference plane are included?
What receiver NF and input losses underlie the specification?
What antenna-noise assumptions were used?
ENAE 694 • Noise and the Link Budget
54

## Slide 54
Lesson Review
Questions: Putting It All Together
Why should the LNA be close to the antenna?
Which LNA parameters reduce total receiver noise?
What does G/T tell us that receiver NF alone cannot?
Which S/N0 terms can the spacecraft or ground provider change?
How would range, weather, or pointing affect the budget?
ENAE 694 • Noise and the Link Budget
55

## Slide 55
Lesson Takeaways
LNA Design and Receiving Sensitivity
LNA placement: minimize loss before the first amplifier.
LNA parameters: low NF and enough early gain reduce receiver noise.*
Receiving system: G/T combines antenna gain with all system noise.
Link trades: more EIRP or G/T improves S/N0.
Propagation, pointing, and polarization losses reduce it.
ENAE 694 • Noise and the Link Budget
56
* Gain must also satisfy overload and stability limits. Antenna and feed noise remain.

## Slide 56
The Complete Link Calculation
The Terms Behind the Trades
EIRP: transmitter power, transmit-line loss, and transmit antenna gain.
Losses: free space, atmosphere, pointing, and polarization.
G/T: receive gain and total system noise at one plane.*
25.2 − 222.6 − 0.1 − 0.8 − 0.5 + 44.7 + 228.6
[S/N0] = 74.5 dB-Hz
ENAE 694 • Noise and the Link Budget
57
* Receive-feed effects are already in G/T. The constant is −[k] for EIRP in dBW and G/T in dB/K.
[S/N0] = [EIRP] − [Lp] − [Latm] − [Lpoint] − [Lpol] + [G/T] + 228.6

## Slide 57
References: Noise and Receiver Models
ENAE 694 • Noise and the Link Budget
58
JPL DESCANSO, Vol. 10, Ch. 2: System Noise Concepts with DSN Applications
NIST: Johnson-noise thermometry and SI defining constants
JPL, Report 42-143: Follow-up Receiver Noise-Temperature Contribution
Keysight: Noise Figure Application / Noise Concepts
JPL DESCANSO, Ch. 5: HEMT Low-Noise Amplifiers
Analog Devices AN-2622: Selecting an RF Low Noise Amplifier
Complete publication links are in the separate Trusted Sources document.

## Slide 58
References and Further Reading
ENAE 694 • Noise and the Link Budget
59
DSN 810-005, Modules 104 and 105: station and environmental noise
ITU-R P.838-3: rain attenuation; P.618-14: Earth-space propagation
Condon & Ransom, Essential Radio Astronomy, Chs. 1–3
Mini-Circuits PGA-103+: manufacturer LNA specifications
ITU-R P.525-5: free-space attenuation
Images: NASA SVS / LRO; NASA/JPL-Caltech; Mini-Circuits via LCSC
Figures and image credits accompany their slides. Full source links are in the source list.