## Slide 1
Spacecraft Communications
ENAE 694
Signals, Modulation,
and Bandwidth
Dave Israel (disrael@umd.edu)
October 19, 2026

## Slide 2
Tonight’s Agenda
ENAE 694 • Signals, Modulation, and Bandwidth
2
Self-Contained Homework 3 Review
Part 1: Carriers, Bits, Symbols, and Digital Modulation
Part 2: Pulse Shaping, Bandwidth, and Link Performance

## Slide 3
Homework 3, Problem 1: The Question
ENAE 694 • Signals, Modulation, and Bandwidth
3
A circular reflector has D = 0.80 m, f = 7.50 GHz, and aperture efficiency 0.55.
(a) Find peak gain in dBi and full half-power beamwidth (HPBW) in degrees.
(b) Double D at fixed f. Find gain change, new gain, and new HPBW.
(c) Restore D and double f to 15.00 GHz. Find gain change and HPBW. Why is this insufficient to determine the received-power change?

## Slide 4
Homework 3: Gain and Beamwidth
Worked Answer
ENAE 694 • Signals, Modulation, and Bandwidth
4
Case | Gain [G] (dBi) | Change (dB) | HPBW (°)
D = 0.80 m, f = 7.50 GHz | 33.37 | Reference | 3.50
Double D to 1.60 m | 39.39 | +6.02 | 1.75
Double f to 15.00 GHz | 39.39 | +6.02 | 1.75
[G] = 17.81 + 20 log₁₀(D) + 20 log₁₀(f)
HPBW ≈ 21/(fD)°. D in m, f in GHz; efficiency 0.55 included.

## Slide 5
Homework 3: Why Gain Alone Is Insufficient
ENAE 694 • Signals, Modulation, and Bandwidth
5
Doubling f changes both antenna gain and free-space loss.
Δ[S] = Δ[GTX] + Δ[GRX] − Δ[Lp] − Δ[Lother]
What Stays Fixed? | Changes at Twice the Frequency | Received Power
Ground antenna gain | +6.0 + 0.0 − 6.0 dB | 0.0 dB change
Both physical apertures | +6.0 + 6.0 − 6.0 dB | +6.0 dB change
We must know the ground-antenna assumption and any other frequency-dependent losses.

## Slide 6
Homework 3, Problem 2: The Question
ENAE 694 • Signals, Modulation, and Bandwidth
6
Aligned, polarization-matched [Pr0] = −118.00 dBW. Required received power = −123.50 dBW. All other losses are included.
Transmit HPBW = 3.50°, error = 0.875°. Receive HPBW = 1.40°, error = 0.350°. Both polarizations are linear.
(a) Find each pointing loss. (b) At 45° polarization misalignment, find polarization loss, actual received power, and margin. Does it meet the threshold?
(c) Repeat power and margin for 60°. Explain how polarization realignment can restore the link without changing peak antenna gain.

## Slide 7
Homework 3: Pointing Loss
Worked Answer
ENAE 694 • Signals, Modulation, and Bandwidth
7
[Lpoint] = 12(θ / HPBW)², using full HPBW and consistent angular units.
Transmit: [Lpt] = 12(0.875 / 3.50)² = 0.75 dB
Receive: [Lpr] = 12(0.350 / 1.40)² = 0.75 dB
Total pointing loss = 0.75 + 0.75 = 1.50 dB. Subtract it once.
The supplied near-boresight approximation does not describe sidelobes or nulls.

## Slide 8
Homework 3: Polarization and Margin
Worked Answer
ENAE 694 • Signals, Modulation, and Bandwidth
8
Axes Differ By | [Lpol] (dB) | [Pr] (dBW) | Margin (dB)
45° | 3.01 | −122.51 | +0.99: meets threshold
60° | 6.02 | −125.52 | −2.02: fails threshold
[Lpol] = −10 log₁₀(cos²ψ)
[Pr] = −118.00 − 1.50 − [Lpol]
Margin = [Pr] − (−123.50 dBW)

## Slide 9
Homework 3, Problem 3: The Question
ENAE 694 • Signals, Modulation, and Bandwidth
9
Nadir-pointed science + continuous communications through a 12-minute overhead pass.
Time (min) | Fixed Gain Offset | Extra Path Loss
0–2 / 10–12 | −8 dB | 4 dB
2–5 / 7–10 | −2 dB | 1 dB
5–7 | 0 dB | 0 dB
At midpass, peak margin = +5 dB. Margin ≥ 0 is usable.
Find fixed and ideal gimbaled margins. Which meets both requirements?
The gimbal holds peak gain, with no added loss. Why can’t we rotate the spacecraft?

## Slide 10
Homework 3: Margin During the Pass
Worked Answer
ENAE 694 • Signals, Modulation, and Bandwidth
10
Time (min) | Fixed Gain (dB) | Extra [Lp] (dB) | Fixed Margin (dB) | Gimbal Margin (dB)
0–2 | −8 | 4 | −7 | +1
2–5 | −2 | 1 | +2 | +4
5–7 | 0 | 0 | +5 | +5
7–10 | −2 | 1 | +2 | +4
10–12 | −8 | 4 | −7 | +1
Margin = 5 + gain relative to peak − extra path loss.
Fixed: usable only 2–10 min. Gimbal: usable throughout the pass.
The gimbal restores peak gain; it does not remove the extra path loss.

## Slide 11
Homework 3, Problem 4: The Question
ENAE 694 • Signals, Modulation, and Bandwidth
11
Keep the science and continuous-communications requirements from Problem 3. Installed antenna-system mass limit = 5.0 kg.
Option A: 2.0 kg fixed antenna. Option B: 6.0 kg gimbaled antenna. Both have the RF performance used in Problem 3. Mass includes feed, supports, and mechanisms.
(a) Which requirements does each option meet? Does either meet all? (b) Recommend a feasible change and state its cost or performance consequence.
(c) Why does antenna mass location affect spacecraft slewing and pointing even when total mass is unchanged?

## Slide 12
Homework 3: Mass and Pointing
Worked Answer
ENAE 694 • Signals, Modulation, and Bandwidth
12
Option | Installed Mass | Communications + Science | All Requirements?
A: Fixed | 2.0 kg; 3.0 kg below limit | Cannot maintain both through full pass | No: loses link at pass ends
B: Gimbaled | 6.0 kg; 1.0 kg above limit | Tracks station while science stays nadir-pointed | No: exceeds mass limit
Neither option meets every requirement as proposed.
The limit is 5.0 kg. Turning the spacecraft toward the station would violate the required nadir science attitude.

## Slide 13
Homework 3: The Engineering Trade
ENAE 694 • Signals, Modulation, and Bandwidth
13
Reallocate at least 1.0 kg to permit the 6.0 kg gimbaled system. Other hardware must give up that mass allocation.
Alternatively, redesign the gimbaled system to 5.0 kg or less while retaining RF and pointing performance. Verify the redesigned hardware.
Mass farther from a rotation axis contributes more rotational inertia: I = Σmr² for point masses. This affects slew torque and settling.
*Problem 4(c) is outside this course’s scope. Everyone receives full credit for that part.

## Slide 14
Clarifications From October 5
ENAE 694 • Signals, Modulation, and Bandwidth
14
[1, 2]
An absorbing atmosphere weakens the signal and emits thermal noise.
Off the lunar disk means the line of sight is outside the apparent Moon.
S/N0 compares signal power with noise per hertz. Its units are dB-Hz.
Noise factor F is linear. Noise figure NF = 10 log₁₀(F) is in dB.
T0 = 290 K: a common reference near room temperature.
It makes component NF values comparable. It is not the actual antenna or hardware temperature.
Another reference changes reported NF; consistent Te = (F − 1)T0 gives the same physical noise.

## Slide 15
What Information Does a Signal Carry?
ENAE 694 • Signals, Modulation, and Bandwidth
15
[3, 4]
Command Uplink
Telemetry / Science Return
The waveform also provides timing, range, and Doppler measurements.
*Conceptual AI-generated illustration [15]. Sizes, distance, and signal paths are schematic.

## Slide 16
The Spacecraft Communications Chain
ENAE 694 • Signals, Modulation, and Bandwidth
16
[11, 12]
SPACECRAFT
GROUND STATION
Avionics and RF hardware
inside the spacecraft bus
Antenna and feed
launch the radio wave
Return Link
C&DH
Encode /
Modulate
PA
TX
Antenna
RX
Antenna
LNA
Demodulate /
Decode
C&DH collects data. PA = power amplifier.
Low-loss RF feed connects PA to antenna.
Ground receiver and mission-data processing.
Keep loss before the LNA small.
Photos: LRO, NASA/GSFC [11]; Goldstone, NASA/JPL-Caltech [12]. Functional locations are schematic; DSN beam-waveguide optics carry RF to receiver equipment.

## Slide 17
Why Put Information on a Carrier?
ENAE 694 • Signals, Modulation, and Bandwidth
17
[3]
Chart: Information: Bit Levels
Chart: Carrier: Fixed Frequency fc
×
Modulator
Chart: Output: Phase Carries the Bits
The data selects the carrier phase.
The antenna radiates the RF output.
Low-rate information moves to a band suited to antennas and spectrum allocation.
Illustrative BPSK. Only a few RF cycles per bit are drawn so the phase changes are visible. fc is the carrier frequency.

## Slide 18
Bits, Line Coding, and Symbols
ENAE 694 • Signals, Modulation, and Bandwidth
18
[3, 6]
Chart: NRZ-L
Bits: 1 0 1 1 0 0 1 0
A bit is a binary value. A symbol is one selected transmitted waveform.
Line coding turns a bit stream into a baseband waveform.
NRZ and Manchester encode the same bits with different transitions.

## Slide 19
Bit Rate and Symbol Rate
ENAE 694 • Signals, Modulation, and Bandwidth
19
[3, 6]
Bit rate Rb: information bits per second.
Symbol rate Rs: selected waveforms per second.
SAME EIGHT BITS
1
0
1
1
0
0
1
0
BPSK: 1 bit / symbol
1
0
1
1
0
0
1
0
8 symbols
QPSK: 2 bits / symbol
1 0
1 1
0 0
1 0
4 symbols
Rs = Rb / (bits per symbol)
At 1.0 Mbit/s: BPSK = 1.0 Msymbol/s; QPSK = 0.5 Msymbol/s.
Two identical consecutive states still occupy two symbol intervals.

## Slide 20
Line Coding Changes the Transitions
ENAE 694 • Signals, Modulation, and Bandwidth
20
[3, 6]
Chart: NRZ-M
Bits: 1 0 1 1 0 0 1 0
NRZ-L holds a level for each bit interval.
NRZ-M changes level on a chosen bit value. Manchester changes at every bit center.
More transitions can aid timing recovery, but require more bandwidth.

## Slide 21
Time Domain and Frequency Domain
ENAE 694 • Signals, Modulation, and Bandwidth
21
[3]
Chart: Rectangular-pulse spectrum
A waveform shows how the signal changes with time.
The Fourier transform gives its frequency-domain description.
Abrupt transitions spread signal energy into sidelobes.

## Slide 22
On-Off Keying
ENAE 694 • Signals, Modulation, and Bandwidth
22
[3, 6]
Chart: OOK
One state sends a carrier. The other sends no carrier.
The information changes the carrier amplitude.
For unbalanced on/off levels, a residual carrier component may remain.

## Slide 23
Frequency-Shift Keying
ENAE 694 • Signals, Modulation, and Bandwidth
23
[3, 6]
Chart: FSK
A 0 and a 1 select different carrier frequencies.
The receiver decides which tone is present.
Required bandwidth depends on tone spacing and pulse shaping.

## Slide 24
BPSK: A Bit Selects the Carrier Phase
ENAE 694 • Signals, Modulation, and Bandwidth
24
[3, 6]
Chart: BPSK
Binary phase-shift keying uses two phases separated by 180°.
One bit per modulation symbol.
For rectangular bit pulses, null-to-null RF bandwidth is approximately 2Rb.

## Slide 25
BPSK: Two Possible Decisions
ENAE 694 • Signals, Modulation, and Bandwidth
25
[3, 6]
Chart: Ideal Symbol States
| -1
Symbol 1 | 0
Symbol 2 | 0
I
Q
A constellation shows symbol states after carrier removal.
I = in-phase (horizontal). Q = quadrature (vertical), relative to the carrier reference.
Ideal BPSK has two I values and Q = 0. Each point represents one possible symbol.

## Slide 26
QPSK: Two Bits per Symbol
ENAE 694 • Signals, Modulation, and Bandwidth
26
[3, 6]
Chart: Ideal Symbol States
| -0.8
Symbol 1 | -0.8
Symbol 2 | 0.8
Symbol 3 | 0.8
Symbol 4 | -0.8
I
Q
Four carrier phases represent four possible two-bit symbols.
Each transmitted symbol carries two bits.
For an uncoded QPSK link, Rs = Rb / 2.

## Slide 27
Summary: Amplitude, Frequency, and Phase
ENAE 694 • Signals, Modulation, and Bandwidth
27
[3, 6]
Chart: The Same Data Controls Each Carrier
Data
0 / 1
Amplitude
ASK
Frequency
FSK
Phase
BPSK
1
0
1
1
0
0
1
0
Vertical lines mark bit boundaries. The data waveform shows actual transitions; adjacent equal bits need no state change. Waveforms are illustrative.

## Slide 28
The I and Q View of a Modulator
ENAE 694 • Signals, Modulation, and Bandwidth
28
[3, 6]
Serial bits
Serial-to-
Parallel
×
×
+
I(t)
Q(t)
Carrier
Oscillator
+90°
cos(2πfc t)
−sin(2πfc t)
RF Output
s(t) = I(t) cos(2πfc t) − Q(t) sin(2πfc t)

## Slide 29
Question: BPSK or QPSK
ENAE 694 • Signals, Modulation, and Bandwidth
29
Uncoded information rate = 1.0 Mbit/s. Keep received power, noise density, and pulse shaping fixed. Change BPSK to QPSK. Which statement is correct?
A. Symbol rate halves, so the RF bandwidth is about halved.
B. The received energy per information bit doubles.
C. The symbol rate doubles.

## Slide 30
Worked Answer: BPSK or QPSK
ENAE 694 • Signals, Modulation, and Bandwidth
30
A. Half the Symbol Rate and RF Bandwidth
Rs = Rb / bits per symbol: BPSK = 1.0 Msymbol/s; QPSK = 0.5 Msymbol/s.
B is false: fixed power and information rate give the same energy per bit. C is false: symbol rate halves.
At a fixed SYMBOL rate instead, QPSK carries twice as many information bits per second.

## Slide 31
Break
ENAE 694 • Signals, Modulation, and Bandwidth
31
Next: Pulse Shaping, RF Bandwidth, and the Complete Eb/N0 Budget

## Slide 32
Pulse Shaping: The Same Bits in Time
ENAE 694 • Signals, Modulation, and Bandwidth
32
[3, 13]
Chart: Without Explicit Pulse Shaping
Chart: Root-Raised-Cosine Transmit Shaping
Abrupt
transitions
Smooth,
overlapping
pulses
Same eight bits and symbol rate. Only the transmit pulse shape changes.
Normalized baseband voltage, uncoded BPSK. RRC roll-off α = 0.35. Pulse overlap is intentional; a matched receiver controls interference at decision instants.

## Slide 33
Pulse Shaping: RF Bandwidth and Sidelobes
ENAE 694 • Signals, Modulation, and Bandwidth
33
[3, 13]
Chart: Same Symbol Rate: 1.0 Msymbol/s
Rectangular: first-null span = 2Rs = 2.0 MHz; sidelobes extend beyond it.
Ideal RRC: RF span = (1 + α)Rs = 1.35 MHz. Practical filters need allowances.

## Slide 34
Pulse Shaping: Benefits and Costs
ENAE 694 • Signals, Modulation, and Bandwidth
34
[13, 14]
Benefit | Cost or Constraint
Lower out-of-band emissions | Transmit and receive filters must work together
More controlled channel bandwidth | Filter memory and timing affect symbol decisions
Closer channel spacing | Conventional RRC-shaped BPSK* can need amplifier backoff
More efficient use of spectrum | Choose a waveform compatible with the spacecraft amplifier
*RRC = root-raised cosine. Saturation can distort envelope variations and regrow sidelobes.
GMSK (Gaussian minimum-shift keying) and selected shaped OQPSK (offset QPSK) can offer favorable amplifier behavior.

## Slide 35
Bandwidth Example: BPSK and QPSK
ENAE 694 • Signals, Modulation, and Bandwidth
35
[3]
Assumptions | BPSK | QPSK
Information rate Rb | 1.0 Mbit/s | 1.0 Mbit/s
Bits per symbol | 1 | 2
Symbol rate Rs | 1.0 Msymbol/s | 0.5 Msymbol/s
BRF at α = 0.35 | 1.35 MHz | 0.68 MHz
Uncoded examples. BRF = (1 + α)Rs. Both transmit the same number of information bits each second.

## Slide 36
Direct Modulation and Subcarriers
ENAE 694 • Signals, Modulation, and Bandwidth
36
[4, 6]
Chart: Direct BPSK
Chart: BPSK on 70 kHz Subcarrier
Data spectrum is centered on the RF carrier.
Data sidebands move to ±70 kHz.
*Calculated average spectra: uncoded 10 kbit/s NRZ, no pulse shaping. PSD relative to unit complex-envelope power/Hz. No receiver noise; display stops at −80 dB/Hz.

## Slide 37
Residual Carrier With a BPSK Subcarrier
ENAE 694 • Signals, Modulation, and Bandwidth
37
[4]
Chart: Illustrative RF Spectrum
Residual Carrier | -55 | -3
Lower Sideband
Residual Carrier
Upper Sideband
−1.024 MHz
0
+1.024 MHz
32 kbit/s BPSK on a 1.024 MHz subcarrier
*Illustrative power allocation. Unshaped NRZ data: each sideband has a 64 kHz first-null span.

## Slide 38
Data Power Is Part of Total Signal Power
ENAE 694 • Signals, Modulation, and Bandwidth
38
[4]
Illustrative Allocation of Total Received RF Power
Ranging 20%
Residual Carrier 30%
Data 50%
100% of Total RF Power
q = Sdata / Stotal = 0.5
[Sdata/N0] = [Stotal/N0] + 10 log₁₀(q)
For q = 0.5, data-channel S/N0 is 3.0 dB lower.
*Assumed power fractions sum to 100%. Modulation indices and waveform design determine the actual split. The diagram shows allocation, not signal flow.

## Slide 39
Modulation Selection Is a Mission Trade
ENAE 694 • Signals, Modulation, and Bandwidth
39
[3, 4, 6]
Need | Signal Design Implication
Weak signal acquisition | Consider tracking aids and residual-carrier power
High data rate in limited spectrum | More bits per symbol and appropriate pulse shaping
Efficient spacecraft power amplifier | Control envelope variation and amplifier backoff
Navigation or tracking on the same link | Allocate signal power and spectrum to each function
Choose the waveform with the receiver, amplifier, and mission requirements in view.

## Slide 40
The Receiver Must Recover the Bits
ENAE 694 • Signals, Modulation, and Bandwidth
40
[3, 5]
RF / IF
Conversion
Carrier + Timing
Recovery
Filter + Symbol
Decisions
Channel
Decoder
The receiver needs carrier and timing references before making symbol decisions.
Its error performance depends on signal energy relative to noise.
Next class examines the receiver and decoder in detail.

## Slide 41
Bit Errors and Mission Performance
ENAE 694 • Signals, Modulation, and Bandwidth
41
[5, 7]
1,000,000 Bits
BER = 10−5
10 Bit Errors on Average
Measured BER = erroneous bits / tested bits
A theoretical bit-error probability predicts long-run behavior under stated assumptions.
At BER = 10−5, one million bits contains 10 errors on average.
A mission may require frame or packet error performance, not only raw BER.

## Slide 42
Energy per Information Bit
ENAE 694 • Signals, Modulation, and Bandwidth
42
[3, 7]
Energy per Bit = Received Data Power ÷ Information Bit Rate
Eb = Sdata / Rb
J/bit = (J/s) ÷ (bit/s)
Eb/N0 = (Sdata/N0) / Rb
[Eb/N0] = [Sdata/N0] − 10 log₁₀(Rb / 1 bit/s)
At fixed data power, twice as many bits each second means half the energy per bit: −3.0 dB.

## Slide 43
Lunar Link: Available Eb/N0
ENAE 694 • Signals, Modulation, and Bandwidth
43
Carry forward [Sdata/N0] = 74.5 dB-Hz. Assume all signal power carries data.
At Rb = 1.0 Mbit/s:
[Eb/N0] = 74.5 − 10 log₁₀(1,000,000) = 14.5 dB
At Rb = 2.0 Mbit/s: 74.5 − 63.0 = 11.5 dB

## Slide 44
Question: Doubling the Information Rate
ENAE 694 • Signals, Modulation, and Bandwidth
44
Keep received data power and noise density fixed. Double information rate from 1.0 to 2.0 Mbit/s. What changes?
A. Eb/N0 improves by 3.0 dB
B. Eb/N0 worsens by 3.0 dB
C. S/N0 worsens by 3.0 dB

## Slide 45
Worked Answer: Doubling the Information Rate
ENAE 694 • Signals, Modulation, and Bandwidth
45
B. Available Eb/N0 Falls by 3.0 dB
[Eb/N0] = [Sdata/N0] − [Rb]. Rate rises from 60.0 to 63.0 dB(bit/s).
Sdata/N0 stays 74.5 dB-Hz. Available Eb/N0 falls from 14.5 to 11.5 dB.
A has the sign reversed. C is false because the received power and noise density stay fixed.

## Slide 46
The Ideal BPSK and QPSK BER Curve
ENAE 694 • Signals, Modulation, and Bandwidth
46
[7]
Chart: Coherent BPSK / Gray QPSK
BER target (0.00001) | -5 | -5
−5 on the vertical axis means BER = 10−5.
Coherent BPSK and Gray QPSK in AWGN:
Pb = ½ erfc(√(Eb/N0))
Eb/N0 inside the square root is a linear ratio.
At BER = 10−5, the ideal requirement is approximately 9.6 dB.

## Slide 47
Reading a BER Curve
ENAE 694 • Signals, Modulation, and Bandwidth
47
[7]
Eb/N0 | Ideal Uncoded BER | Interpretation
6.0 dB | 2.4 × 10−3 | About 2,400 errors per million bits
9.6 dB | 9.7 × 10−6 | About 10 errors per million bits
12.0 dB | 9.0 × 10−9 | Far fewer errors under this ideal model
Coherent BPSK, AWGN, perfect synchronization. Actual equipment adds implementation effects.

## Slide 48
Available and Required Eb/N0
ENAE 694 • Signals, Modulation, and Bandwidth
48
[3, 7]
Available Eb/N0 comes from received data power, noise density, and information rate.
Required Eb/N0 comes from a performance curve or a tested receiver specification.
Example: ideal coherent uncoded BPSK needs about 9.6 dB for BER = 10−5 in AWGN.
Real receiver losses and design reserve must also fit in the budget.

## Slide 49
Lunar Link: Closing the Margin
ENAE 694 • Signals, Modulation, and Bandwidth
49
Available [Eb/N0] = [Sdata/N0] − [Rb] = 74.5 − 60.0 = 14.5 dB
Assume BER ≤ 10−5 requires 9.6 dB for ideal uncoded BPSK.
Assume a separate implementation loss of 1.0 dB.
Margin = 14.5 − 9.6 − 1.0 = 3.9 dB

## Slide 50
Lunar Link: Rate and Margin
ENAE 694 • Signals, Modulation, and Bandwidth
50
Information Rate | Available Eb/N0 | Margin*
1.0 Mbit/s | 14.5 dB | 3.9 dB
2.0 Mbit/s | 11.5 dB | 0.9 dB
4.0 Mbit/s | 8.5 dB | −2.1 dB
*Margin = 74.5 − 10 log₁₀(Rb) − 9.6 − 1.0 dB. Bandwidth and lock must also be adequate.

## Slide 51
Question: The 4 Mbit/s Link
ENAE 694 • Signals, Modulation, and Bandwidth
51
We need 3.0 dB reserve, but the 4.0 Mbit/s case has −2.1 dB margin. Which change alone is enough?
A. Switch BPSK to QPSK at the same information rate
B. Reduce the information rate to 1.0 Mbit/s
C. Add 20 dB of ideal gain after the receiver front end

## Slide 52
Worked Answer: The 4 Mbit/s Link
ENAE 694 • Signals, Modulation, and Bandwidth
52
B. Reduce the Information Rate
The 1.0 Mbit/s case has 3.9 dB margin and exceeds the 3.0 dB reserve.
A reduces bandwidth but does not change ideal bit-energy performance.
C amplifies signal and existing noise together.

## Slide 53
Lunar Link: The Remaining Trades
ENAE 694 • Signals, Modulation, and Bandwidth
53
[3, 5, 7]
Change | Budget Effect | Mission Cost
More data-channel EIRP | More available Eb/N0 | Spacecraft power or antenna demands
Better G/T or lower losses | More available Eb/N0 | Ground hardware, siting, or operations
Lower information bit rate | More energy per information bit | Longer delivery time
Different modulation / coding | May lower required Eb/N0 | Bandwidth, complexity, or latency
A lower requirement must come from a justified performance comparison at the same delivered error target.

## Slide 54
The Complete Link Equation
ENAE 694 • Signals, Modulation, and Bandwidth
54
[3, 4, 7]
[Eb/N0] = [EIRP] − [Lp] − [Lother] + [G/T] − [k] + [q] − [Rb]
[q] = 10 log₁₀(q), where q is the fraction of received signal power allocated to data.
[Rb] = 10 log₁₀(Rb / 1 bit/s), using the information bit rate.
[k] = −228.6 dBW/Hz/K. G and Tsys use the same reference plane.
Available Eb/N0 must cover the requirement, implementation loss, and reserve.

## Slide 55
What If the Link Still Does Not Close?
ENAE 694 • Signals, Modulation, and Bandwidth
55
We have optimized power, antennas, receiver noise, losses, and data rate.
Our available Eb/N0 still falls short of the requirement.
Could we transmit the bits in a way that requires less Eb/N0?
Next Class: Demodulation, BER, and Coding

## Slide 56
Optional Reference Slides
ENAE 694 • Signals, Modulation, and Bandwidth
56
Additional Signal Examples and Calculation Details

## Slide 57
Why the 290 K Reference Cancels
ENAE 694 • Signals, Modulation, and Bandwidth
57
[2]
Chosen Reference T0 | Reported Noise Factor F | Recovered Receiver Te
290 K | 2.0 (NF = 3.0 dB) | (2.0 − 1) × 290 = 290 K
Hypothetical 580 K | 1.5 (NF = 1.8 dB) | (1.5 − 1) × 580 = 290 K
Te = (F − 1)T0. Same hardware, different reporting convention. Actual output noise = GkB(TA + Te), unchanged by the reference choice.

## Slide 58
Pulse-Shape Mismatch: A Numerical Example
ENAE 694 • Signals, Modulation, and Bandwidth
58
[3, 13]
Receive Filter | Required Eb/N0 at BER = 10−5
Matched root-raised-cosine filter | 9.6 dB
Rectangular integrate-and-dump filter | 10.5 dB
Additional required Eb/N0 | About 1.0 dB
*Teaching calculation: uncoded BPSK, RRC transmit roll-off 0.35, AWGN, perfect carrier/timing, independent bits, no equalizer. This penalty is specific to these assumptions.

## Slide 59
Navigation and Tracking Signals
ENAE 694 • Signals, Modulation, and Bandwidth
59
[4]
Purpose | Observable or Reference | Example
Navigation | Known timing/code/phase references | GPS time-tagged ranging codes
Historical navigation | Carrier Doppler over a pass | Transit navigation
Bearing reference | Carrier/subcarrier phase relationship | VOR
Spacecraft tracking | Range and Doppler over time | Orbit estimation
Range is a line-of-sight distance measurement. Doppler constrains line-of-sight velocity; a trajectory solution uses measurements over time.

## Slide 60
Frequency Bands and Spectrum Access
ENAE 694 • Signals, Modulation, and Bandwidth
60
[10]
S, X, Ku, and Ka are useful space-communications bands. L, VHF, and UHF also serve particular missions.
Available bandwidth depends on the allocated service, direction, region, and authorization.
Higher-frequency links can offer wider allocations while facing tighter pointing and weather trades.
A band name alone does not guarantee a usable bandwidth or non-line-of-sight coverage.

## Slide 61
Subcarrier Examples and Ranging Tones
ENAE 694 • Signals, Modulation, and Bandwidth
61
[4]
Direct example: 100 kbit/s telemetry modulates the RF carrier without an added subcarrier.
Subcarrier example: place 100 kbit/s data on a 1.024 MHz subcarrier. Account for both RF sidebands.
Combined example: 20 kbit/s telemetry on a 70 kHz subcarrier, plus ranging tones at 4, 20, 100, and 500 kHz.
These are illustrative plans. Modulation indices set the power split; receiver compatibility sets usable combinations.
PN ranging uses a known pseudo-random pattern and correlation. It need not use a telemetry subcarrier.

## Slide 62
Analog Modulation Equations
ENAE 694 • Signals, Modulation, and Bandwidth
62
[3, 6]
AM: s(t) = A[1 + μm(t)] cos(2πfc t)
FM: s(t) = A cos[2πfc t + 2πkf ∫m(τ)dτ]
PM: s(t) = A cos[2πfc t + kp m(t)]
For FM, Carson’s approximation is B ≈ 2(Δf + fm,max).
No blanket AM/FM/PM performance ranking applies without assumptions.

## Slide 63
Manchester, NRZ, and Timing Recovery
ENAE 694 • Signals, Modulation, and Bandwidth
63
[3, 6]
Chart: NRZ-M
Bits: 1 0 1 1 0 0 1 0
Long runs without transitions make timing recovery harder.
Manchester guarantees a transition at each bit center.
NRZ schemes can use scrambling or other structure to aid timing.
A line-code symbol, a coded bit, and an RF modulation symbol are different concepts.

## Slide 64
Higher-Order Constellations
ENAE 694 • Signals, Modulation, and Bandwidth
64
[3, 6]
Chart: Ideal Symbol States
| -1.5
Symbol 1 | -1.5
Symbol 2 | -0.5
Symbol 3 | 0.5
Symbol 4 | 1.5
Symbol 5 | -1.5
Symbol 6 | -0.5
Symbol 7 | 0.5
Symbol 8 | 1.5
Symbol 9 | -1.5
Symbol 10 | -0.5
Symbol 11 | 0.5
Symbol 12 | 1.5
I
Q
M-PSK places more phase states on a circle. QAM uses amplitude and phase.
More coded bits per symbol can reduce the required symbol rate.
At fixed average symbol energy, more closely spaced states are harder to distinguish.
Envelope variation and amplifier linearity become important.

## Slide 65
Lunar Link: Maximum Rate With Reserve
ENAE 694 • Signals, Modulation, and Bandwidth
65
Require 3.0 dB design reserve beyond the BER requirement and implementation loss.
[Rb,max] = 74.5 − 9.6 − 1.0 − 3.0 = 60.9 dB(bit/s)
Rb,max = 1060.9/10 ≈ 1.2 Mbit/s
This is a power-limited result. Spectrum, coding, hardware, and acquisition can lower it.

## Slide 66
Lunar Link: Reference Planes
ENAE 694 • Signals, Modulation, and Bandwidth
66
Quantity | Antenna Terminals A | LNA Input B
Received signal | −131.9 dBW | −132.9 dBW
Equivalent system temperature | 168.0 K / 22.3 dBK | 133.5 K / 21.3 dBK
Equivalent noise density | −206.3 dBW/Hz | −207.3 dBW/Hz
S/N0 | 74.5 dB-Hz | 74.5 dB-Hz
Same complete system represented at two planes. B includes receiver-added noise referred to its input. Inserting a lossy cable physically still degrades the link.

## Slide 67
References and Further Reading
ENAE 694 • Signals, Modulation, and Bandwidth
67
[1] NRAO. Essential Radio Astronomy, Chapter 1: atmospheric attenuation and emission.
[2] Keysight. Noise Figure application help: thermal noise and the 290 K reference.
[3] R. Gallager. MIT 6.450, Chapter 6: Channels, Modulation, and Demodulation.
[4] JPL. DSN Telecommunications Link Design Handbook, 810-005, Module 206: Telemetry General Information.
[5] CCSDS 131.0-B-5 (2023). TM Synchronization and Channel Coding.

## Slide 68
References and Further Reading
ENAE 694 • Signals, Modulation, and Bandwidth
68
[6] Keysight. Digital Modulation in Communications Systems, Application Note 1298.
[7] MathWorks. Analytical Expressions Used in berawgn Function and Bit Error Rate Analysis App.
[8] CCSDS 130.1-G-3 (2020), with technical corrigendum: TM Synchronization and Channel Coding, Summary of Concept and Rationale.
[9] MIT 6.450, Lecture 23: channel capacity and the wideband energy limit.
[10] NTIA. United States Frequency Allocation Chart and Table of Frequency Allocations.

## Slide 69
References and Image Credits
ENAE 694 • Signals, Modulation, and Bandwidth
69
[11] NASA/Goddard Space Flight Center. LRO Assembly and Testing Stills, SVS 10408. Spacecraft photograph.
[12] NASA/JPL-Caltech. Goldstone 34-meter Beam Waveguide, PIA17791. Ground antenna photograph.
[13] MathWorks. Raised Cosine Filtering and Raised Cosine Receive Filter documentation.
[14] CCSDS 413.0-G-3, with Technical Corrigendum 1. Bandwidth-Efficient Modulations, Sections 3 and Annex B.
[15] Spacecraft–Earth scene: AI-generated conceptual illustration. Distances and sizes are not to scale.